## Slide 1: Monitoring of Instrumentation for Critical Nuclear Fusion Plasma Control and Data Acquisition Systems
Name: Paulo Fortuna Carvalho
Email: pricardofc@ipfn.ist.utl.pt
5th PhD Event, Prague, Czech Republic, 15-18 November, 2015

## Slide 2: Main Topics
Introduction: Control in Nuclear Fusion Plasmas
Purpose
Why Monitoring?
Why ATCA and uTCA Systems?
ATCA Control and Data Acquisition System
System Components
Software Modules
Hardware Management
External System Management
Conclusions
References

## Slide 3: Purpose
Development of a System Manager Application for Monitoring and Management of a Control and Data Acquisition System Hardware.

## Slide 4: Control in Nuclear Fusion Plasmas is Critical for Safe Operation and to Achieve High Performance
Density
Control
Magnetic control
Position, Shape & Vertical Stabilization
Wall Protection
Instabilities Mitigation & Control
Malfunction of a single component may originate Critical Damage to entire infrastructure!

## Slide 5: Why Monitoring?
Nuclear Fusion Plasmas Behavior Study and Understanding. How?
Monitoring and Hardware Management to AVOID Instrumentation Failure!
Demands Critical Realtime Tasks to Prevent Machine Components DAMAGE and Plasma Termination!
Answer: Control and Data Acquisition Instrumentation
Plasma Shape, Positioning and Vertical Stabilization
Fusion Reactor
(Tokamak)
Diagnostics
Fusion Reaction
Acquisition and Feedback Control

## Slide 6: Why ATCA and uTCA Systems? Implementation and tests will take place on ATCA platform (Ref.1) but can be used with other form factors such as uTCA.
s
uATCA Shelf
ATCA 5-slot
Shelf
ATCA 14-slot
Shelf
Provide
High Availability
Serviceability
Redundancy
High Reliability
Modularity
High Data Throughput
Required by diagnostics in these kind of Fusion Experiments!

## Slide 7: ATCA Control and Data Acquisition System
Host
Computer
PCI Express
Cable
ATCA 14-slot
Shelf
ATCA-PTSW-AMC4
ATCA-IO-PROCESSOR
RTM Module
RTM Module
Figure 1. ATCA System Components Overview.

## Slide 8: C&DAQ (Ref. 2)
ADC module , 1-2 MSPS, 18 bit
with ADC x2 and chopper mode
DAC module
with DAC x2
IPMC
CoreIPM OPMA2368 Module
ATCA-IO-Processor
CDaQ Board
RTM Module
Figure 9. ATCA-IO-PROCESSOR Control and Data Acquisition Card.
Features
48 Channels
  48 Inputs (Max.)
  48 Output (Max.)
  Mixed (I/O)
16 bits Resolution
@ 200MSPS (Max.)

## Slide 9: Hub Switch (Ref. 3)
Benefits
  Timing
  Synchronism
  Endpoints
    System Hierarchy
    Access
    Detection
  Host Link
  PCI Express
    Hotplug
    Communication
  ATCA Hotswap
ATCA-PTSW-AMC4
Time Switch Board
RTM Module
Figure 8. ATCA-PTSW-AMC4 Time
Switch Card.
AMC
FMC
Module
AMC
FMC
Module
AMC
FMC
Module
AMC
FMC
Module

## Slide 10: Hardware Management Levels
Monitoring
  Sensors reading
  Alarm handling
  Error detection and correction
  System health status
  System events logging
Maintenance
  Hotplug and hotswap capabilities
  System availability
  System redundancy
  Reliability and serviceability
Safety Operation
  Hardware/software electronic keying (e-keying)
System Inventory
  FRU information
  Sensor data records
Figure 11. ATCA Management
Levels Overview.

## Slide 11: Management Interface Platforms
Intelligent Platform Management Interface
  IPMI library implementation
  IPMC firmware interface (Ref. 4)
Shelf Management (ATCA/MTCA based instrumentation)
  ShM management controllers firmware
Hardware Platform Interface
  Standard software architecture model
External System Management Application
  Including Java/EPICS framework/CSS user interface (End-User)
  Including distributed and redundant databases and redundant server PCs.

## Slide 12: ATCA Hardware Architecture
External System
Manager
Shelf Manager
(Active)
Shelf Manager
(Backup)
Shelf Manager Controller
Shelf Manager Controller
Board
IPMC
RTM
Board
Board
Fan Tray
PEM Module
RTM
RTM
Carrier
IPMC
AMC
AMC
MMC
MMC
Carrier
IPMC
MMC
IPMC
IPMC
IPMB-L
IPMB-L
2x Redundant IPMB-0
2x Redundant Ethernet (optional)

## Slide 13: Software Modules
Features
  Linux Device Drivers API
  System Services
  Graphical User Interfaces
    Java Applications
    Control System Studio OPIs
    C/C++ Applications
  Firmware
  Console Applications
  Shell Scripts
  ITER-CODAC Interface
  EPICS Framework
Benefits
  Control Room Operation
  System Maintenance
  HW Components Status Monitoring
Figure 10. JET Control Room Monitoring, Control and System Operation.

## Slide 14: Communication Protocols
Figure 13. ATCA External System Manager Software Architecture.
Description
External Sys Manager
  TCP/IP
  IPMI Over LAN
    Shelf Manager Controller
      I2C (IPM Controller)
  PCI Express
    Hardware Access
      Acquisition
      Card Configuration

## Slide 15: Software Design
Figure 11. Software Architecture Internal Mechanism Block Diagram.
External System Manager can use the HPI and IPMI platforms to query the ShMC for system information, status and sensor readings.
Waits for response from IPMCs to inform a control room operator about the system healthy status and notify in case of alarm occurences.
System log to store important realtime events ocurring in the system to provide later analysis and report capabilities.

## Slide 16: Software Architecture
Figure 12. Software Architecture Internal Communication Protocols Block Diagram.
Inter-layer connection is performed in a top-down perspective using the common standard communication protocols provided by the required instrumentation specifications.

## Slide 17: System Maintenance
Damaged Hardware
Unit Replacement Required
HW Availablility Check
Provide System Operation
  Continuous (Reduces Data Losses)
  Applications Proper Termination
Provided by Redundancy
  In Software Modules
  In Hardware Components
AMC
AMC
AMC
AMC
ATCA-PTSW-AMC4
Time Switch Board
RTM Module

## Slide 18: Hotswap Procedure
1
2
5
1st Card Working
Card can be Removed
2nd Card
Ready
3
4
Remove 1st Card
Insert 2nd Card, Switch ON Handle, Wait for Green Led
Switch OFF Handle
Wait for Hotswap Blue Led

## Slide 19: Hotswap Benefits
Damaged Unit Replacement
No Entire System Shutdown Required
Continuous Operation

## Slide 21
(Ref.5)

## Slide 23: Conclusions
Guarantees better response to control and data acquisition systems failures.
Prevents plasma disruptions in nuclear fusion experiments and tokamak machine components damages.
Allows acquisition transfers with less data losses operating in a non-stop environment.
Provides system information, acquisition and configuration, safety operation, simplifies hardware maintenance, allows local or remote software and firmware upgrades and system databases updates.
Ensures fusion power plant preservation, avoids instrumentation failure, grants people and environment protection.

## Slide 24: References
ITER prototype fast plant system controller based on ATCA platform, B. Goncalves · J. Sousa · B. B. Carvalho · A Batista · A Neto · B. Santos · A Duarte · D. Valcarcel · D. Alves · M. Correia · [...] · N. Utzel · P. Makijarvi · C Leong · V Bexiga · I C Teixeira · J P Teixeira · A Barbalace · P Lousa · J Godinho · P Mota, Proc. IEEE Nuclear Science Symp. and Medical Imaging Conf. (NSS/MIC); 01/2011
Control and data acquisition ATCA/AXIe board designed for high system availability and reliability of nuclear fusion experiments, A.J.N. Batista · C. Leong · V. Bexiga · A.P. Rodrigues · A. Combo · B.B. Carvalho · P.F. Carvalho · J. Fortunato · B. Santos · P. F. Carvalho · M. Correia · J.P. Teixeira · I.C. Teixeira · J. Sousa · B. Goncalves · C.A.F. Varandas
Timing distribution and synchronization of an ATCA fast controller for fusion devices, M. Correia · J. Sousa · B.B. Carvalho · A. Combo · A.P. Rodrigues · A.J.N. Batista · B. Santos · P.F. Carvalho · B. Goncalves · C.M.B.A. Correia · C.A.F. Varandas, Real Time Conference (RT), 2012 18th IEEE-NPSS; 01/2012
Intelligent Platform Management Controller Software Architecture in ATCA Modules for Fast Control Systems, A. P. Rodrigues · Miguel Correia · A. Batista · P. R. Carvalho · Bruno Santos · B. B. Carvalho · J. Sousa · B. Gonçalves · C. M. B. Correia · C. A. F. Varandas, IEEE Transactions on Nuclear Science 01/2012; 61(4). DOI:10.1109/RTC.2012.6418387
The ITER Fast Plant System Controller ATCA prototype Real-Time Software Architecture, B.B. Carvalho · B. Santos · P.F. Carvalho · A. Neto · L. Boncagni · A.J.N. Batista · M. Correia · J. Sousa · B. Gonçalves

## Slide 25
Thank You!