## Slide 1
ITER: the next step
R. A. Pitts Experiments and Plasma Operation Section, Science Division ITER organization
IDM UID: CCUH2M
The views and opinions expressed herein do not necessarily reflect those of the ITER Organization.
Czech Technical University Prague, 24 October 2024, Czech Republic

## Slide 2: Outline
Introduction: what is ITER?
  The ITER machine and main goals
  Partnership and procurement sharing
The ITER site today, delivery of major components and how the tokamak is assembled
  A brief summary in pictures of machine assembly
  Issues found on vacuum vessel sectors and thermal shields
The ITER Research Plan and “re-baselining”
  New schedule to First Plasma and first Burning Plasma

## Slide 3
Thousands of engineers and scientists have contributed to the design of ITER since the idea for an international joint experiment in fusion was first launched in 1985. The ITER Members: China, the European Union, India, Japan, Korea, Russia and the United States, are now engaged in a 35-year collaboration to build and operate the ITER experimental device, and together bring fusion to the point where a demonstration reactor can be designed
First, what is the ITER Project
The ITER Organization is an intergovernmental organization, formally established on 24 October 2007
It aims to promote cooperation among the ITER members (Domestic Agencies (DA)) that are involved in the development of ITER.
It also acts as the overall integrator of the project and nuclear operator of the ITER facility.

## Slide 4
The ITER machine
ITER is the largest tokamak ever built.
It will produce plasmas that create more fusion energy than needed to heat them (Q > 1) and be dominantly heated by the fusion reactions themselves (Q > 5), with a primary target of Q = 10 at a plasma current of 15 MA  burning plasmas:
  Major radius: 6.2 m
  Toroidal field and current: 5.3 T and 15 MA
  Combined stored magnetic energy: ~50 GJ
  Plasma volume: >800 m3
  Nominal auxiliary heating power: 73 MW
  Fusion power: 500 MW
  Vacuum Vessel volume: 1000 m3
  Device weight: ~23,000 tonnes
  Cryostat: 29 m wide, 29 m high, 16,000 m3
R ~ 6.2 m
h ~ 29 m

## Slide 5
ITER will maintain burning fusion plasmas for long periods of time. It will test the integrated technologies, materials, and physics regimes necessary for the commercial production of fusion-based electricity.

## Slide 6
ITER
Fusion gain and ITER
ITER☼
Fusion energy gain:
a-heating fraction:
Q = 1 | fa = 17%
Q = 5 | fa = 50%
Q = 10 | fa = 67%
Q = 20 | fa = 80%
Q =  | fa = 100%
Breakeven
Burning plasma regime
  ITER is designed to a scale which should yield Q ≥ 10 at a fusion power of 400 – 500 MW for 300 – 500 s  Baseline Scenario
R. A. Pitts et al., Physics World 19 (2006) 20

## Slide 7: An updated Lawson plot
S. Wurzel, S. Hsu, Phys. Plasmas. 29 (2022) 062103
NIF (Inertial Fusion, LLNL, USA) Milestone in Dec. 2022 with 2.05 MJ laser energy used to produce 3.15 MJ fusion energy  Q = 1.5
(NB: only a small fraction (~1%) of the laser input power is reflected from the walls of the Hohlraum onto the DT target)

## Slide 8: An updated Lawson plot
S. Wurzel, S. Hsu, Phys. Plasmas. 29 (2022) 062103
FRC type approaches generally still very far behind the curve in terms of energy breakeven and fusion gain

## Slide 9: An updated Lawson plot
S. Wurzel, S. Hsu, Phys. Plasmas. 29 (2022) 062103
New private industry tokamak (https://cfs.energy/)  uses high BT approach and plans to use DT fuel.
Pfusion  BT4
Competes with ITER in terms of ntT (and Q), but only for very short pulse lengths (few seconds)  major simplification cf. ITER (no active cooling and only small quantities of tritium required)

## Slide 10
E  Ip R2 P-2/3
ITER basis: energy confinement
Energy confinement difficult to predict quantitatively  use scalings from experiments + plasma physics limits to dimension ITER to achieve its goals
  Baseline is Type I ELMing H-mode  robust mode of operation in today’s tokamaks
  IPB98(y,2) Type-I ELMing H-mode scaling
q95 = 3
R

## Slide 11
ITER Q = 10 scenario (300 – 500 s burn)
Based on conventional sawthoothing H-mode with H98 = 1  scenario used for design of magnets and components
Paux = PNBI + PECH (+PICH) ~ 50 MW  alpha-heating dominant scenario with ~35% non-inductively driven curent

## Slide 12
Baseline heating and current drive systems
NB: subject to change in the re-baseline

## Slide 13
Diagnostics and 3D coils (Error field, ELM control)
Diagnostics: ~60 instruments, measuring ~100 parameters, many used in real time  used as part of a sophisticated, system-engineered plasma control system
External error field correction coils (superconducting) + internal ELM control coils (not superconducting)

## Slide 14: Nuclear operation: tritium breeding modules (TBMs)
Tritium fuel cycle is a major challenge for all DT fusion devices  needs to be produced in-situ (n + Li)
A principal technology goal of ITER is to demonstrate T-production schemes (at small scale)
  Different test blanket systems will be installed to test different combinations of design options:
  Liquid metal breeder
  Solid breeder
  Helium coolant
  Water coolant

## Slide 15
Disruptions a major issue
PC08
1 barrel
1 barrel
1 barrel
Upper ports
PC02
PC14
6 barrels
6 barrels
12 barrels
PC08
PC02
PC17
Equatorial ports
Massive programme on ITER to design, test and build a reliable and robust “Disruption Mitigation System” (DMS)
  Based on multiple cryogenic (H, Ne) shattered pellet injection (SPI) to dissipate thermal and current quench energies and to prevent the formation of, or kill runaway electron beams

## Slide 16: ITER construction sharing
IO Staff distribution by Member (December 2023)
8.7%
2.5%
4.0%
6.2%
7.9%
3.8%
64.6%
2.4%
A unique feature of ITER is that almost all (~90%) of the machine will be constructed through in-kind procurement from the Parties
Overall sharing: EU: 5/11 Other 6 Members: 1/11 each
Notes: 2022: 1 IUA = 1,822.33 Euro (see https://user.iter.org/?uid=6VUGL9)
1 kIUA =

## Slide 17: Who manufactures what?
All intellectual property is shared by the seven members
Toroidal Field Coils (18)
Poloidal Field Coils (6)
Thermal Shield
Vacuum Vessel
Blanket
Feeders (31)
Divertor
Central Solenoid (6)
Correction Coils(18)
Cryostat

## Slide 18: The ITER site today (see: https://www.iter.org/news/galleries for much, much more)

## Slide 19: ITER platform: a brief recap
21 Jan. 2007
French Alternative Energies and Atomic Energy Commission (CEA) acquires ~180 hectares for the ITER Project, near the CEA Cadarache nuclear research centre
CEA Cadarache centre

## Slide 20
29 Jan. 2009
1000 long, 400 m wide, the ITER platform ready for construction

## Slide 21
27 Sept 2023
ITER construction site drone view

## Slide 22
27 Sept 2023
Cryostat upper cylinder (temporary storage)
Assembly Hall
RF Building
Tritium building
Tokamak building
Heat rejection system
Main control room
Magnet power conversion buildings
PF coil winding facility
Cryoplant
Cryostat workshop
400 kV switchyard
Diagnostics building
ITER Organization HQ
Transformers
ITER construction site drone view
Component storage area

## Slide 23
20 June 2024
Latest available drone view

## Slide 24
25 novembre 2021
Cryoplant Largest single unit plant in the world. Liquid He inventory 25 t Power: 75 kW at 4.5 K (He) 1300 kW at 80 K (N2)
Over 5000 t of equipment installed in the cryoplant in 3.5 years
He gas compressor and gas distribution network completed functional tests in July 2024  first liquid He to be made this year  support operation of a Magnet Cold Test Bench (TF coil tests)
Notes: tanks, compressors, piping, valves, electrical motors, gas bags

## Slide 25
15 octobre 2021
~6000 t of equipment supplied by IN-DA  commissioning well underway
Cooling plant Optimise management of an intermittent demand (peak: 1145 MW, between pulses: 160 MW)

## Slide 26
25 mars 2021
Electrical conversion ~5 km of actively cooled busbars 100% of the equipment necessary for First Plasma installed

## Slide 27
29 August 2023
Bridging gaps …. Cryobridge and busbar bridges for distribution of cryolines and transport of electrical busbars

## Slide 28
August 2024
Pulse-power electrical network (PPEN) is in operation Supplied by two 400 kV lines connected to the French grid
Full energization of the 1st of 3 bays complete

## Slide 29
ITER Control Room Main construction complete
29 August 2023

## Slide 30
Status of selected major components

## Slide 31
Nearly 10,000 tonnes of superconducting magnets (niobium-tin, Nb3Sn or niobium-titanium Nb-Ti)
Reminder: the ITER main magnet systems
  Combined total stored energy of 51 GJ
  Highly complex system of cryogenics and coil feeders (31)

## Slide 32
PF coils:
NbTi, 6 T, 45 kA, largest coils (PF 3,4) 24 m diameter, 400 t
PF6 (CN), PF5 (EU): complete and in-pit PF1, 2 (RF, EU): complete and in storage PF3,4 (EU): complete and in storage
15 Apr. 2024
PF3: being moved into storage
PF3 completed

## Slide 33
TF coils:
NB3Sn, 11.8 T, 68 kA, 41 GJ, 9 x 17 m, 360 t each
JA: 9 coils  9 on-site
EU: 10 coils: 10 on-site
8 July 2022
15 Dec. 2023
TF18 – last EU coil arrives on-site

## Slide 34
Central solenoid: one of the most massive components of the ITER machine. 6-module stack, mass >1000 t, Nb3Sn, Stack height ~20 m high, ~4 m wide, max. current ~46 kA
4 modules now on-site (supplied by US-DA (General Atomics)). Last two arrive in 2025.
Two modules on the stack in Sept. 2023
3rd CS module now added
11 Apr. 2024

## Slide 35
Error field correction coils NbTi, max current ±10 kA, 6x6 coils, largest 8.4 x 7.2 m, total mass 78 t All Top and Bottom coils delivered, delivery of 6 side coils in 2026
Installation of one of the lower (bottom) correction coils (BCC)
21 Oct. 2021
Joint manufacturing for SCC4
August 2024

## Slide 36
Cryostat: pit assembly completed for Base Section and Lower Cylinder. Upper Cylinder and Top lid completed and in long term storage
10 March 2022
Being moved to long term storage location

## Slide 37
KO: 3 Sectors 6,7,8 at IO
Sector 1 completed and in France But repairs required – see later
EU: Sector 5 (Walter Tosto, Italy) complete and in France – the first of the EU sectors – arrival at ITER site 25/10 (tomorrow)!
24 Sept. 2024
Vacuum Vessel: 9 sectors (KO: 4 sectors, EU: 5 sectors)

## Slide 38
EU VV Sector 5 being transported by barge across the inland sea Étang de Berre
11 Oct. 2024
15 Oct. 2024
KO VV Sector 1 being offloaded at Fos-sur-Mer – expected at the ITER site early November

## Slide 39
Very brief resumé of machine assembly activities in the last ~3 years

## Slide 40
Tokamak Pit painted up and ready for first major components
26 May 2020

## Slide 41
The first big lift: 1250 tonne, 30 m diameter cryostat base on its way to the pit
26 May 2020
SSAT-1
SSAT-2
These massive Sub-Sector Assembly Tools (SSAT), supplied by Korea, are used for assembly of complete vacuum vessel sectors weighing ~1400 tonnes

## Slide 42
The first big lift: 1250 tonne, 30 m diameter cryostat base on its way to the pit
26 May 2020

## Slide 43
Next up: 375 tonne lower cryostat cylinder
31 August 2020

## Slide 44
Lower cylinder thermal shield on its way
14 Jaunuary 2021

## Slide 45
Lower cylinder of in-pit Assembly Tool
27 March 2021
Temporary supports for PF6
Full assembly
17 August 2021

## Slide 46
First poloidal field coil PF6 inserted onto temporary supports
21 April 2021
Toroidal field coil gravity supports

## Slide 47
Radial beam testing  beams carry each VV sector and must be very precisely positioned
7 September 2021

## Slide 48
PF 5 coil lifted into the tokamak pit
15 September 2021

## Slide 49
8 December 2021
PF5
PF6
Metrology and adjustment

## Slide 50
20 December 2021
Tokamak Pit ready for the first VV sector

## Slide 51
Assembly and installation of first complete VV sector

## Slide 52
In February 2021, Assembly Hall being prepared for first VV Sector upending
28 February 2021
VV Sector 6 being prepped for upending

## Slide 53
Start of upending sequence to place Sector 6 into the vertical position
26 March 2021
Done!

## Slide 54
Final step: transfer to the SSAT
6 April 2021
Rail transport structure the same system which is used to hold the sector in place for in-pit installation

## Slide 55
And finally, inserted from above into the SSAT
6 April 2021

## Slide 56
Inboard thermal shield section clamped to Sector 6
21 June 2021

## Slide 57
Full VV thermal shield on, Sector 6 and TF12 now on SSAT-2
12 August 2021

## Slide 58
Just prior to final positioning of TF coils
30 August 2021

## Slide 59
First complete Sector 6 ready for pit installation
15 November 2021

## Slide 60
VV Sectors 6 and 7 both on SSAT tools
3 January 2022

## Slide 61
The first sector lift and placement – a major milestone for the project

## Slide 62
Sector 6 fully lifted out of SSAT-2 and rotated 90
11 May 2022

## Slide 63
11 May 2022
Sector 6 fully lifted out of SSAT-2 and rotated 90

## Slide 64
11 May 2022
Over the tokamak pit wall: 20 cm gap

## Slide 65
11 May 2022
Lowering into the tokamak pit

## Slide 66
14 June 2022
In-place and alignment procedure underway

## Slide 67
Sept. 2022
Final alignment complete. Sector placed to millimetric precision according to physics specifications

## Slide 68
Dimensional non-conformities in VV field joint contours on the 3 sectors delivered to IO have turned out to be too large to permit sector-sector welding according to required standards
  https://www.iter.org/newsline/-/3818
  and
  https://www.iter.org/newsline/-/3830
Chloride stress corrosion cracking (SCC) found on many of the thermal shield cooling pipes
More details of these issues and their solution were released publicly:
And now the bad news …..
Major issues preventing continued assembly of VV sectors

## Slide 69
SCC on thermal shields: problem found on several VV shields not yet installed on VV sectors  assumed to be present in many locations in VV and cryostat shields

## Slide 70
Some areas of non-conformity on VV field joints, particularly where the individual VV segments are joined
2 June 2023

## Slide 71
For the VV thermal shield  remove old pipes and re-weld new ones (different steel and welding process/material) + re-manufacture of a few panels
For the cryostat thermal shield  leave old pipes (but don’t connect) and re-weld new ones in-situ (different steel and welding process/material)
Solutions
For VV non-conformity  remove and add material to meet required dimensions (~73 – 400 kg per sector)

## Slide 72
VV Thermal Shields: repair and replacement
  Inboard
  (IB)
  Outboard
  Left Hand side (OBLH)
  Equatorial port
  Shrouds
  Outboard
  Right hand side (OBRH)
2nd CCTS OBRH pre-assembly test (INOX, India)
Repairing 7 VVTS sets (21 panels)
Remanufacturing 2 VVTS sets (6 panels)
  Replace corroded pipes
  2 mm panel machining to eliminate potential panel corrosion risk
  Surface polishing to replace silver coating  roughness < 0.1 mm  low emissivity at 80 K
Progressing well

## Slide 73
VV bevel joint repairs
Sectors 6, 7 repaired in vertical position (SSAT)
Sectors 1, 8 in horizontal position (Cryostat Building)
Before repair
After repair
SP
INNER BEVEL
OUTER BEVEL
T-RIB
INNER BEVEL
OUTER BEVEL
S06
S07
SP100

## Slide 74
5th July 2023
First full sector module coming back out of the pit for dismantling and repair on an SSAT

## Slide 75
8 Feb. 2024
Back in the SSAT, TF coils and thermal shields removed. Repairs carried out in parallel by a consortium of Italian firms

## Slide 76
18 July 2024
Repairs in-situ on Sectors 6, 7
Sector 7
Sector 6

## Slide 77
15 July 2024
Sector 8 under repair (horizontally) in repurposed cryostat workshop

## Slide 78
15 Sept 2024
Sector 7: repair complete, re-assembly underway with repaired VVTS
Sector 5 (on-site for 25/10): repaired at supplier
Sector 6 (at ITER): repairs in progress  forecast 15/11/2024
Sector 8 repairs in progress  forecast 25/07/2025
Sectors 2,3,4,9: manufacturing in progress (at EU supplier)

## Slide 79: The ITER Research Plan and “re-baselining”

## Slide 80
Robust achievement of ITER Project goals, in view of current and past challenges (delays due to the Covid-19 pandemic, technical challenges in completing first-of-a-kind components and in nuclear licensing)
Realistic and reliable assembly – commissioning - operation
Achievement of earliest start of the ITER Nuclear Phase (DD operation) and minimization of technical risks
Stepwise Safety Demonstration
SRO (Start of Research Operation) and DT-1,2 phases
New Baseline rationale
Key elements of the new baseline:
    First Wall: beryllium (Be)  tungsten (W)
    Optimized heating mix + boronization  ease path to Q = 10 with added W

## Slide 81
ITER is a very large step from present day magnetic confinement devices
Complexity, large uncertainties and very ambitious project goals make a safety demonstration in “one go” very challenging
Stepwise Safety Demonstration
Phase 2: DT-2
Second phase of safety demonstration with knowledge acquired during DT-1
Attain lifetime neutron fluence  3 x 1027 neutrons
Phase 1: DT-1
A first phase of safety demonstration of ITER operation developed
Focused on the achievement of specific project goals
Limited neutron fluence (1% of present “end-of-life” Project Specification)  ~3 x 1025 neutrons

## Slide 82
Physics basis for tokamak operation with W walls is much stronger than it was at start of ITER construction
Several issues with Be as PFC: Erosion lifetime
    Tritium retention in co-deposits
    Low melting point  lower margin in Ip before potential “gap bridging” on FW panels (disruption current quench)
Major benefit in assembly complexity and avoid costly later wall changeout
Why change to a tungsten First Wall?
Be
Beryllium
4
9.012
W
Tungsten
74
183.84
Tmelt = 1287C
Tmelt = 3422C
BUT: lose low Z material facing the plasma and gettering properties of Be

## Slide 83
New Baseline Phases and Research Plan
R. A. Pitts, PSI 2024

## Slide 84
Updated timing …. (proposal to ITER Council)

## Slide 85
Thanks for your attention
IDM UID: CCUH2M
Czech Technical University Prague, 24 October 2024, Czech Republic
R. A. Pitts Experiments and Plasma Operation Section, Science Division ITER organization