## Slide 1
01/16
EC waves in COMPASS and COMPASS-U tokamaks
Michal Farník
FTTF workshop Mariánská 2020
xx/xx
M. Farník: ECRH / FTTF / 2020

## Slide 2
Part I. ECRH for COMPASS-U
  Specifications
  Simulations
  To Do
Part II. V-ECE for RE measurements in COMPASS
  Introduction
  Simulations
  Measurements
Summary
01/16
xx/xx
M. Farník: ECRH / FTTF / 2020

## Slide 3
01/16
xx/xx
M. Farník: ECRH / FTTF / 2020
Thermal ECE: B ~ 1/R → spacial resolution of ECE, ECA and ECRH (Te and heating)
Nonthermal ECE: Emmited frequency is dependent also on the particle position in the velocity phase (v → c)
Electron cyclotron (EC) waves are caused by the gyro-motion along the external magnetic field

## Slide 4
01/16
Part I. ECRH for COMASS-U
1/12
M. Farník: ECRH / FTTF / 2020

## Slide 5
COMPASS-U will be equipped with an NBI heating system. An additional ECRH heating is planned on the tokamak.
Main features of the ECRH:
01/16
2/12
M. Farník: ECRH / FTTF / 2020

## Slide 6
COMPASS-U will be equipped with an NBI heating system. An additional ECRH heating is planned on the tokamak.
Main features of the ECRH:
Heating
Improving H-mode performance
01/16
2/12
M. Farník: ECRH / FTTF / 2020

## Slide 7
COMPASS-U will be equipped with an NBI heating system. An additional ECRH heating is planned on the tokamak.
Main features of the ECRH:
Heating
Improving H-mode performance
Preventing impurity accumulation (W) in the core
Suppressing Neoclasical Tearing Modes (NTMs)
01/16
2/12
M. Farník: ECRH / FTTF / 2020

## Slide 8
COMPASS-U will be equipped with an NBI heating system. An additional ECRH heating is planned on the tokamak.
Main features of the ECRH:
Heating
Improving H-mode performance
Preventing impurity accumulation (W) in the core
Suppressing Neoclasical Tearing Modes (NTMs)
Current Drive (ECCD) – profile tailoring
01/16
2/12
M. Farník: ECRH / FTTF / 2020

## Slide 9
01/16
3/12
M. Farník: ECRH / FTTF / 2020
COMPASS-U: DEMO relevant research (R0 = 0.894 m, a = 0.27 m) Extreme power fluxes - up to 70 MW/m2 - liquid metal technology Operation with high temperature first wall – up to 600°C BT = 5 T Ip = 2 MA tflattop = 1-5 s ne: ~ 1020 m-3 PNBI = 4-5 MW PECRH = 2-10 MW

## Slide 10
01/16
3/12
M. Farník: ECRH / FTTF / 2020
COMPASS-U: DEMO relevant research (R0 = 0.894 m, a = 0.27 m) Extreme power fluxes - up to 70 MW/m2 - liquid metal technology Operation with high temperature first wall – up to 600°C BT = 5 T Ip = 2 MA tflattop = 1-5 s ne: ~ 1020 m-3 PNBI = 4-5 MW PECRH = 2-10 MW
1st harmonic heating (high BT)
140 GHz Considered (AUG,W7-X)
O-mode: cutoff density 2.51020 m-3 X-mode: core achievable from the HFS

## Slide 11
01/16
3/12
M. Farník: ECRH / FTTF / 2020
COMPASS-U: DEMO relevant research (R0 = 0.894 m, a = 0.27 m) Extreme power fluxes - up to 70 MW/m2 - liquid metal technology Operation with high temperature first wall – up to 600°C BT = 5 T Ip = 2 MA tflattop = 1-5 s ne: ~ 1020 m-3 PNBI = 4-5 MW PECRH = 2-10 MW
1st harmonic heating (high BT)
140 GHz Considered (AUG,W7-X)
O-mode: cutoff density 2.51020 m-3 X-mode: core achievable from the HFS

## Slide 12
Scenarios: |  |  |  |  |  | 
# | Bt [T] | Ip [MA] | tflattop [s] | ECRH | fECRH [GHz] | ncut [1020 m-3]
2.4 | 1.25 | 0.4 | 4.3 | 3rd harm. X-mode | 105 | 0.9
3.4 | 2.50 | 0.8 | 3.2 | 2nd harm. X-mode | 140 | 1.2
4.4 | 4.30 | 1.4 | 1.5 | 1st harm. O-mode | 140* | 2.5
6.4 | 5.00 | 2.0 | 1.0 | 1st harm. O-mode | 140* | 2.5
 | *planned upgrade to 250-280GHz system |  |  |  |  | 
01/16
4/12
M. Farník: ECRH / FTTF / 2020

## Slide 13
Scenarios: |  |  |  |  |  | 
# | Bt [T] | Ip [MA] | tflattop [s] | ECRH | fECRH [GHz] | ncut [1020 m-3]
2.4 | 1.25 | 0.4 | 4.3 | 3rd harm. X-mode | 105 | 0.9
3.4 | 2.50 | 0.8 | 3.2 | 2nd harm. X-mode | 140 | 1.2
4.4 | 4.30 | 1.4 | 1.5 | 1st harm. O-mode | 140* | 2.5
6.4 | 5.00 | 2.0 | 1.0 | 1st harm. O-mode | 140* | 2.5
 | *planned upgrade to 250-280GHz system |  |  |  |  | 
Variables:
Launcher placement – equatiorial vs. upper port
Toroidal and poloidal angle adujstement
Density (!!!) – unofortunately we are close to cutoff
01/16
4/12
M. Farník: ECRH / FTTF / 2020

## Slide 14
TORBEAM
Beam tracing code - calculation of propagation and absorption of an EC wave beam in a tokamak plasma
The paraxial WKB approximation
Set of ODEs – Gaussian beam
Diffraction effects – deposition profiles
01/16
5/12
M. Farník: ECRH / FTTF / 2020

## Slide 15
Equatorial port Poloidal angle scan
Scenario 3.4
B = 2.5 T → 2nd harmonic heating central density ne = 0.95∙1020 m-3
01/16
6/12
M. Farník: ECRH / FTTF / 2020

## Slide 16
Upper port Poloidal angle scan
Scenario 3.4
B = 2.5 T → 2nd harmonic heating central density ne = 0.95∙1020 m-3
01/16
7/12
M. Farník: ECRH / FTTF / 2020
Diff. theta → edge deposition

## Slide 17
Upper port Poloidal angle scan
Scenario 3.4
B = 2.5 T → 2nd harmonic heating central density ne = 0.95∙1020 m-3
01/16
7/12
M. Farník: ECRH / FTTF / 2020
57° - all power deposited
Diff. theta → edge deposition

## Slide 18
Upper port Poloidal angle scan
Scenario 3.4
B = 2.5 T → 2nd harmonic heating central density ne = 0.95∙1020 m-3
01/16
7/12
M. Farník: ECRH / FTTF / 2020
58° - No deposited power
57° - all power deposited
Diff. theta → edge deposition

## Slide 19
Scenario 3.4
B = 2.5 T → 2nd harmonic heating
01/16
8/12
M. Farník: ECRH / FTTF / 2020
Density determines the eventual shine-through of the beam, that would result in serious damage on the plasma-facing components (PFCs)
No significant power deposition on HFS PFCs → no need for reflecting tile

## Slide 20
Equatorial port Toroidal angle scan
Scenario 4.4
B = 4.3 T → 1st harmonic heating central density ne = 2∙1020 m-3
01/16
9/12
M. Farník: ECRH / FTTF / 2020

## Slide 21
Scenario 6.4
B = 5.0 T → 1st harmonic heating central density ne = 2∙1020 m-3
Equatorial port Toroidal angle scan
01/16
10/12
M. Farník: ECRH / FTTF / 2020

## Slide 22
Equatorial injection → narrow deposition
Small beam divergence - no need for focusing mirror
Safe operation up to 1.05∙1020 m-3
Scenario 3.4:
01/16
11/12
M. Farník: ECRH / FTTF / 2020
Scenario 4.4:
Off-axis heating
Toroidal angle necessary to deposit power closer to the core
Focusing mirror necessary
Safe operation up to 2.2∙1020 m-3
Scenario 6.4:
Strong beam divergence in higher densities
Safe operation up to 2.2∙1020 m-3
Current drive with toroidal angle injection (~10 kA)
All the power is absorbed. (if beam reaches resonance layer)
Common:

## Slide 23
Effect of ECRH and ECCD on profiles
Next steps:
01/16
12/12
M. Farník: ECRH / FTTF / 2020

## Slide 24
Effect of ECRH and ECCD on profiles
ECRH assisted breakdown
Optimisation of NTM suppresion efficiency
Next steps:
01/16
12/12
M. Farník: ECRH / FTTF / 2020

## Slide 25
Effect of ECRH and ECCD on profiles
ECRH assisted breakdown
Optimisation of NTM suppresion efficiency
Just design the ECRH system
Next steps:
01/16
12/12
M. Farník: ECRH / FTTF / 2020

## Slide 26
01/16
Part II. V-ECE for RE measurements in COMPASS
1/6
M. Farník: VECE / FTTF / 2020

## Slide 27
01/16
2/6
M. Farník: VECE / FTTF / 2020
Vertically placed antenna (V-ECE) → B const along the LoS (and θ π/2)
Relation between the measured frequency and electron velocity
Nonthermal ECE:

## Slide 28
01/16
2/6
M. Farník: VECE / FTTF / 2020
Vertically placed antenna (V-ECE) → B const along the LoS (and θ π/2)
Relation between the measured frequency and electron velocity
Nonthermal ECE:

## Slide 29
01/16
3/6
M. Farník: VECE / FTTF / 2020
Parameters:
Heterodyne ECE/EBE radiometer
13 channels in function
Range: 76,5 - 88,3 GHz
Detection of reflected waves → change of the energy spectrum (various B-field)

## Slide 30
01/16
3/6
M. Farník: VECE / FTTF / 2020
Parameters:
Heterodyne ECE/EBE radiometer
13 channels in function
Range: 76,5 - 88,3 GHz
Detection of reflected waves → change of the energy spectrum (various B-field)
2nd harmonic – 0 - 130 keV 3rd harmonic – 0 - 450 keV 4th harmonic – 75 - 775 keV 5th harmonic – 220 - 1100 keV
in B = 1.15 T discharges

## Slide 31
01/16
4/6
M. Farník: VECE / FTTF / 2020
SPECE code simulations
Electron emissivity is dependent on the electron velocity
Thermal emission negligible due to the strong attenuation of the radiometer.

## Slide 32
01/16
4/6
M. Farník: VECE / FTTF / 2020
SPECE code simulations
Electron emissivity is dependent on the electron velocity
Thermal emission negligible due to the strong attenuation of the radiometer.
Two orders of magnitude difference

## Slide 33
01/16
5/6
M. Farník: VECE / FTTF / 2020
V-ECE measurements
Reliable measurements of RE seed → presence od REs before disruption
V-ECE can be used as a precursor for RE beam generation during a disruption
Only qualitative output → simulations of RE population needed
The same two orders of magnitude difference

## Slide 34
01/16
6/6
M. Farník: VECE / FTTF / 2020
V-ECE measurements
Filamentary structures during the beam generation and beam plateau seen as frequent peaks
Ar puff
D puff

## Slide 35
01/16
6/6
M. Farník: VECE / FTTF / 2020
V-ECE measurements
Filamentary structures during the beam generation and beam plateau seen as frequent peaks
Ar puff
D puff

## Slide 36
ECRH would be very favourable at COMPASS-U.
The 140 GHz solution is feasible for all major scenarios with densities under the cutoff.
Diagnostic of EC emission was implemented and used at the COMPASS tokamak.
V-ECE provides information especially about the primary runaway generation at the ramp-up and in the flat-top phase of the discharge.
EC waves are fundamental tool in tokamak physics.
01/16
Last one
M. Farník: ECRH&ECE / FTTF / 2020