## Slide 1: Continuous control on ASDEX-Upgrade tokamak
O. Kudlacek on behalf of:
AUG control group: W. Treutterer, I. Gomez-Ortiz, A. Grater, F. Janky, T. Maceina, B. Sieglin, T. Zehetbauer, G. Raupp
EPFL Lausanne collaborators: F. Felici
TU Eindhoven collaborators: T. Bosman

## Slide 2: Content of the presentation
Kinetic control in fusion machines specifics
Examples of our work on “advanced” control
  Model based control of the electron temperature
  Iterative learning control for electron and ion temperature optimization
Outlook
  Nonlinear state observers developments
  Model based controller design

## Slide 3: I. Kinetic control: challenges from control perspective
Strong non-linearity & coupling of important quantities
  Energy transport ~ Te/Ti, current profile
  Density peaking coupled with temperature peaking
  Current profile ~ Te
Difficulty to measure some of the quantities
  Use of Extended Kalman filter observers
  Development in shot-to-shot based optimization techniques
    Example: Iterative Learning Control
Models can not be always trusted
  No physics models exist yet
  Semi-empirical models have only limited validity range

## Slide 4: II. a: Model based control of the electron temperature
Support of physics studies:
Keep Te profile constant while the beam heating power deposition changes
Actuators: ECRH heating at two locations
Te measurement: state observer RAPTOR
Original heating location
Changed heating location
EC heating location for control

## Slide 5: Controller design: model based technique
Goal: keep Te profile (7 locations) constant by actuating at 2 locations
Control-oriented simulation matched to experimental data
Model based MIMO controller design
  SVD technique used
F. Felici et al, submitted to Nuclear Fusion

## Slide 6: Experimental results
F. Felici et al, submitted to Nuclear Fusion
Controller works for the range scenarios it was designed for
Higher density => stiff Te

## Slide 7: II b: Iterative learning control for electron and ion temperature optimization
Iterative adjustment of heating actuator trajectories to optimize ion and electron temperature
  Te measurable in RT, Ti not
Actuators:
  NBI: heats ~70 % ions, ~30 % electrons in our target scenario
  ECRH: heats electrons only
Target:
  Increase Ti while keeping Te constant by adapting NBI and ECRH heating

## Slide 8: Introduction: Iterative learning control procedure
Match plasma simulation to existing experiment
Derive linear model of plasma response to actuator changes
Define realistic reference for controlled trajectories
Execute experiment and compare real and expected evolution
Update actuator trajectories by solving optimization problem
Preparation:
Experiment execution:
Repeat till you are happy
... or out of experimental time

## Slide 9: Results: control of Te and Ti
Ti reference reached most of the time, Te does not change that much
Next iteration seems to go in the right direction

## Slide 10: Iterative learning control: conclusion
Te and Ti can be in principle optimized on shot-to-shot base
Future applications:
  Optimization of repetitive processes such as plasma startup
  Optimization of quantities that can not be measured in real time

## Slide 11: III. Outlook

## Slide 12: Further development of state observers
Non-measurable quantities
Measurement of the same quantity by multiple diagnostics
  None of the diagnostics is reliable and sufficiently precise for all discharges
  Synthetic diagnostics + control-oriented model
Status: existing state observers
  RAPTOR: [F. Felici et al, Nuclear Fusion 2011]
    electron temperature profile- used in control
    current profile: no RT diagnostics available
    Ion temperature profile: no RT diagnostics available
  RAPDENS: [T. Blanken et al, Fusion Engineering and Design 2018]
    Average density
    Density profile not mature yet
Plans: include additional diagnostics to the state observers
  More diagnostics becoming real time available => add them to observer
  Improvement of the control-oriented models

## Slide 13: Control outlook: towards model based control
Most of our existing controllers are designed on trial-error base
  Switch to model based design (Fenix simulator, next talk)
System identification:
  No models for everything in fusion
    Example: disruption avoidance in the talk of I. Gomez
  Capture basic system dynamics from existing data?
Long term goal:
  No operation limit violation by controller action
Explore proper techniques for this: Model Predictive Control?